Ondes – close-up of Voice and Channel Components
OndeSynth
Blue wires – Voice context
Phase Clocks
Components may exist in both the Voice and Channel contexts. The Channel context manages all of the voices on a given MIDI channel.
The “wires” are technically drawn backwards (see next slide).
They each have a ‘visited’ flag that needs to be reset for every sample, by calling
WiredIntSupplierPool.reset()
These pools are kept in both the Voice and Channel contexts.
Green wires – Channel context
Magenta wires – Synth (global) context
Channel
Voice
OSC1
OSC2
The Phase Clocks live in the Synth context. The main loop advances these for each sample. When an oscillator goes dormant, it removes its phase clock from the Global collection, and on reactivation must add it in again.
Channel inputs
Junction (voice “main”)
Wired int supplier pool
Limiter
(channel “main”)
Mono Main Mix
Echo
LFO
reset()
“Wires” internally to other Voice Components and to outputs from Channel components to Voice inputs are kept in the Voice.
Wires from Channel→Channel Components, and from Voice → Channel Components are kept in the Channel.
Voice → Channel connections must be removed when the voice goes inactive, and re-added when it activates again. The pause() and resume() functions are in charge of that.
The Voice tracks the Voice→Channel connections in a list of ChannelInputs, which pair from the Voice Component’s output to a Channel Component.
Junction (voice “main”)
…

---
Ondes – close-up of Connections
Therefore, these connections (at the Voice level, from a Channel output to a Voice input) can remain when the voice is inactive.
When the voice is inactive, OSC’s output never is polled, so it never calls currentValue()
The arrow is technically backwards on the previous slide. When the “output” of LFO is connected to the “input” of OSC, it means that OSC has a Lambda in its List (inputs) that will return the current value of the LFO.
The voice is thus a directed (possibly cyclic) Graph starting with the Main Mix, going backwards from the perspective of common audio circuitry. The Mixer pulls rather than the sound generators pushing.
Because it can be cyclic (for FM) the ‘visited’ flag on each WiredIntSupplier must be reset for each sample.
LFO output
connected with
OSC input
OSC
List<WiredIntSupplier> inputs
currentValue()
This connection activates the voice, so it must be removed to deactivate the voice. The Voice remembers it in channelnputs, and must:
disconnect on pause() and
reconnect on resume()
Junction output
connected with
Echo input
Junction
List<WiredIntSupplier> inputs
currentValue()

---
Voice → Channel connections need to be disconnected on pause() and reconnected on resume().
The other combinations should be OK without requiring to be unplugged.
Connections to a Voice-level component will be unused when the voice is inactive, so they can remain connected.
 Voice	→ Voice
 Channel	→ Voice
 Voice	→ Channel
Channel → Channel
Input is kept in Voice
Channel-to-Channel connections only ever resume(). They do not pause().
Input is kept in Channel

---
Ondes – Junction output
Each Voice has a single output in the form of a Junction, that all the sub-outputs of the Voice are inputs to. So, other than the channel-level components, the only output
 to disconnect on pause() and reconnect on resume() is the Junction.
OSC3
For output to Channel-context components, they connect to the actual “main” rather than back to the junction, because otherwise all of the Voice Junctions would get the output from all the other ones.
Channel-context components only ever resume(). They never pause()